## Slide 1
STK Shield Plus – Lightning Risk Analysis
Prepared by:
Sara Francis, Senior Scientist, EMA, Inc.

## Slide 2
Demo Background

## Slide 3: Demo Background
EMA’s lightning probability workflow in STK Shield Plus provides a lightning risk analysis, specific to each scenario, to assess the probability and impact of lightning strikes on aircraft and other assets of interest.
  It determines lightning strike likelihood and current amplitudes based on mission profile which allows for design preparations early on
This demo covers two scenarios, a lower risk workflow and a higher risk workflow
The CONOPS factors are used as a weighting value for the probability. Unless some type of mitigation is in place, the CONOP should be assumed to be 1.

## Slide 4: Demo Background
EMA’s lightning probability workflow in STK Shield Plus allows for two modes: risk to amplitude, and amplitude to risk
In Amplitude to Risk mode, the user enters the lightning current amplitude, in order to determine the mission risk. The workflow yields the probability of a catastrophic failure if the aircraft is designed to be hardened to that amplitude, as well as other probabilities.
In Risk to Amplitude mode, the user enters the risk they wish to keep the mission below, in order to determine which lightning current amplitude to design for. The default Risk to Amplitude value is 1E-07. More conservative values would be 1E-08 or 1E-09, while less conservative would be 1E-06.

## Slide 5: Demo Background
The lower risk workflow has an aircraft hold on the runway for 24 hours prior to leaving Miami, FL to Dallas, TX. Florida is one of the most lightning-dense states in the United States, with peaks in the summer months. The scenario occurs in July. The aircraft is a commercial jet with flight elevation 35000 ft. While on the ground, the aircraft is assumed to be near a lightning tower, which lowers the risk from 1 to 0.01.
The higher risk workflow has an experimental aircraft flying from Dallas, TX to Miami, FL and then in a holding pattern in FL before landing, also in July. The aircraft is gathering data on lightning. The aircraft is a smaller jet, with flight elevation 15000 ft. This elevation, along with the holding pattern in FL, increases the likelihood of lightning strike.

## Slide 6
Setting up the STK Scenario

## Slide 7: Setting up the STK Scenario
Open one of the scenarios in the folder
Right click aircraft in Object Browser to view its properties
The aircraft's Route propagator must be in "Aviator" mode

## Slide 8
Setting up Lightning Risk Options

## Slide 9: Lightning Probability Options
Once the aircraft aviator setup is complete, select the lightning probability options workflow
Select Aircraft from Aircrafts dropdown
If the script to run is Risk to Amplitude, then the Risk input is used and that is the maximum allowable risk
If the script to run is Amplitude to Risk, then the Amplitude input is used and that is the amplitude of the lightning strike

## Slide 10: Lightning Probability Options
CONOPS Factors is a list of comma separated values, each value is a probability adjustment defined by the mission description for each segment of the mission
  The number of CONOPS factors must match the number of steps in Aviator
Once the lightning probability options are completed, click Run Workflow to view the results
After the workflow completes, eleven probability graphs will be available in STK and EMC Plus for viewing

## Slide 11
Analyzing Results

## Slide 12: Analyzing Results
25kA
100kA
The figures shown here are Amplitude to Risk Mode. The graph on the left is the PDF of catastrophic given struck at mission periods for amplitude of 25kA, while the graph on the right is for amplitude of 100kA.

## Slide 13: Analyzing Results
25kA
100kA
The figures shown here are Amplitude to Risk Mode. The graph on the left is the assumed probability of catastrophic vs peak current for 25kA, while the graph on the right is for 100kA.

## Slide 14: Analyzing Results
The figures shown here are Risk to Amplitude Mode. The graph on the left is the PDF of catastrophic given struck at mission periods for a risk of 1E-09, while the graph on the right is for 1E-06.
1E-09
1E-06

## Slide 15: Analyzing Results
1E-09
1E-06
The figures shown here are Risk to Amplitude Mode. The graph on the left is the assumed probability of catastrophic vs peak current for a risk of 1E-09, while the graph on the right is for 1E-06.