## Slide 1
STK Shield Plus – Radiation Hardening
Prepared by:
Zach Stevens – Scientist II
Kevin-Druis Merenda – Principal Scientist I and Lead Product Manager

## Slide 2
Demo Background

## Slide 3: Demo Background
Demo Outline
We seek to analyze ionizing dose as a function of depth using a GEO defined orbit from STK.
We will define a material stackup and an orbit in STK, then run the STK Shield Plus analysis on the stackup to retrieve a dose depth curve.
This demo uses the particle transport from the Geant4 code within STK Shield Plus to retrieve dose at each material layer with thicknesses defined by the user.

## Slide 4: Demo Background
Background
Dose depth curves enable users to get an understanding of how effective a spacecraft’s shielding is against high energy particles and analyze dose at critical regions as a function of depth of shielding around them.
Dose naturally decreases as a function of depth, but the rate of decreasing dose depends on the materials used for shielding.
Materials with greater Z-values are more effective at shielding against these high energy particles, but can come at the cost of higher price, weight, or differing conductivity.
Therefore, these high Z-value materials should be used in tandem with cheaper, lower Z-value materials to find a shielding stackup that is both good at minimizing dose but cost effective for the mission.
This workflow for generating dose-depth curves can be used to analyze shielding to find optimized stackups for minimal dose due to materials.

## Slide 5
Setting up the STK Scenario

## Slide 6: Setting up the STK Scenario
Open the provided STK Scenario within the folder to retrieve a preset Scenario with an Aircraft, Ground Vehicle, Place, Satellite, GEOSatellite, and Target.
For this demo we will use the GEOSatellite.
The other objects are used in the other STK Shield Plus demos.

## Slide 7: Opening STK Scenario

## Slide 8
Setting up Radiation Hardening Options

## Slide 9: Setting up RadHard options
Click the RadHard Options in the toolbar on the right.
Satellite: GEOSatellite
Shape: Shell – generates a set of concentric shells in the order of the defined stackup to run radiation transport on
Particle Type: Proton or Electron – generates a dose-depth curve for whichever is selected, using that particle’s spectrum from the STK object. Other particles require a spectrum energy to be set, as they do not draw from the SEET module
End Time: 5400s – how long to run the analysis for
Material Stackup: as shown to the right - different materials change the dose-depth curve due to material properties. More divisions create more resolution to the curve as we sample dose at more layers.
Headless – if headless, will run without opening the Shield Plus GUI, reducing some computational overhead
Click Run Workflow at the bottom to retrieve a dose-depth curve for the defined material stackup.

## Slide 10: Setting up RadHard Options
A bit more detail on the stackups:
In the workflow, materials are generated from the inside out. So, in this example, we will have a 5mm thick sphere of aluminum split into 5 increments on the inside, then a 1mm thick shell around that, also split into 5 increments.
This is so that we can resolve the first millimeter of shielding in high resolution before resolving some of the inner layers in a little less detail

## Slide 11: Setting up RadHard options

## Slide 12
Analyzing Results

## Slide 13: Analyzing Results
The dose-depth curve should be ported back to STK but can also be viewed in the Discovery window by right clicking “Dose vs. Depth” in the Results tree on the left, and clicking “Plot.”

## Slide 14: Analyzing results