## Slide 1
STK Shield Plus – Ray Tracing
Prepared by:
Zach Stevens – Scientist II
Kevin-Druis Merenda – Principal Scientist I and Lead Product Manager

## Slide 2
Demo Background

## Slide 3: Demo Background
Demo Outline
This demo will walk through how to set up the ray tracing workflow via the following:
Open STK Scenario
Apply settings to a premade model by importing a known dose-depth curve onto detectors
Analyze results to view dose on components

## Slide 4: Demo Background
Background
The intent of the ray tracing workflow is to provide estimation of dose at a component level for rapid analysis of radiation shielding on a model.
The workflow traces rays from each mesh node on specified detectors through the geometry around it, applying the provided dose-depth curve to calculate equivalent dose at each node.
This provides estimates of dose on a per-component basis, enabling quick turnaround from analysis to iterative fixes of models.

## Slide 5
Setting up the STK Scenario

## Slide 6: Setting up the STK Scenario
Open the provided STK Scenario within the folder to retrieve a preset Scenario with an Aircraft, Ground Vehicle, Place, Satellite, GEOSatellite, and Target.
For this demo we will use the GEOSatellite.
The other objects are used in the other STK Shield Plus demos.

## Slide 7: Opening STK Scenario

## Slide 8
Setting up Ray Tracing Options

## Slide 9: Setting up Ray Tracing options
Click the Ray Tracing Options button in the top right
Dose Depth Curve – .dat file created via the RadHard workflow, or by Spinvis. For this demo, use the provided Dose Depth Curve (dose_depth_dsne_geo.dat).
Geometry – PCB geometry .dsco file (RayTracing_Tutorial_completed.dsco)
Chassis Thickness – Extra material thickness of the satellite to account for
Rays per Origin – Number of rays per node to sample (the default 20736 is usually ok)
Headless – If headless, runs without opening the Discovery GUI.

## Slide 10: Setting up Ray Tracing options
This model uses a preset model with a simple PCB within the human capsule model, assuming the human capsule is fully made of aluminum.
Detectors are already set on the surface of the board and two components.
We are importing the dose-depth curve from NASA’s Design Specifications for Natural Environments (DSNE) to see what dose on each of these components would be in a worst-case GEO environment.
Detectors

## Slide 11: Setting up Ray Tracing Options

## Slide 12
Analyzing Results

## Slide 13: Analyzing Results
To visualize the Ray-Tracing results, right click on ‘RayTracing_DoseDepth’ in the Results tree on the left of the Discovery window, then click “Ray Tracing Visualization”
On the right, click the Contours button, and dose can then be viewed on the components

## Slide 14: Analyzing results
Highest dose on port edges

## Slide 15: Analyzing Results
To get a more quantitative report of dose per component, open the simulation directory where the .dsco file is saved (\yourfilepath\RayTracing_Tutorial_Completed\Simulation 1\1\) and open “RayTracingReport_All.dat”
This will give you a report similar to below.
DETECTOR | SHIELDING THICKNESS (kg/m^2 ) | EQUIVALENT AL. (m) | ADDED SHIELDING AL. (m) | RAY DOSE (rad) | TOTAL AREA (m^2) | DOSE ESTIMATE (rad) | DOSE ESTIMATE 2 (rad)
Board | 9.25694406e-01 | 3.42596005e-04 | 0.00000000e+00 | 4.62215216e+04 | 3.16721654e-03 | 4.62215216e+04 | 8.35468539e+01
copper_nets1 | 9.65595245e-04 | 3.57363155e-07 | 0.00000000e+00 | 1.45133515e+05 | 1.35383628e-03 | 1.45133515e+05 | 5.96190004e+01
copper_nets5 | 1.19985116e+00 | 4.44060383e-04 | 0.00000000e+00 | 2.34116627e+04 | 1.51752446e-04 | 2.34116627e+04 | 4.48644961e+01

## Slide 16: Analyzing results