## Slide 1
STK Shield Plus – Shielding Effectiveness
Prepared by:
Zach Stevens – Scientist II
Jason Dimartino – Scientist II
Kevin-Druis Merenda – Principal Scientist I and Lead Product Manager

## Slide 2
Demo Background

## Slide 3: Demo Background
Demo Outline
In this demo, we will setup as follows:
Open Shielding Effectiveness Scenario in STK.
Load the Enclosure model in and set mesh resolution.
Investigate shielding results.

## Slide 4: Demo Background
Background
Shielding Effectiveness is a measurement of how well a piece of equipment protects against incoming electromagnetic fields.
We measure this by placing a probe inside the enclosure that we are using to shield, and taking a ratio of signal received inside the enclosure compared to the incoming signal, giving us a transfer function. This is usually achieved using a simple gaussian waveform.
Then, using that transfer function, we can apply that to other incoming more complicated signals to understand the frequency domain response.

## Slide 5
Setting up the STK Scenario

## Slide 6: Setting up the STK Scenario
Open the provided STK Scenario within the folder to retrieve a preset Scenario with an Aircraft, Ground Vehicle, Place, Satellite, and Target.
For this demo we will use Satellite1.
The other objects are used in the other STK Shield Plus demos.

## Slide 7: Opening STK Scenario

## Slide 8
Setting up Shielding Effectiveness Options

## Slide 9: Setting up Shielding Effectiveness options
Click the Shielding Effectiveness Options button in the top right
Graph Object – Any should do here – this is where the results will be propagated back to.
Geometry – Enclosure geometry .dsco file (Shielding_Effectiveness_One_Click_blank.dsco)
Minimum Number of Steps: This controls the mesh resolution across the domain.
Gaussian EM Pulse:
  These settings control the waveform of the incoming EM wave. Default values should be fine.
Direction: This allows for specification of the coordinate axis of propagation for the EM wave.
Headless: if headless, will run without opening the Shield Plus GUI, reducing some computational overhead.

## Slide 10: Setting up Shielding Effectiveness options
This workflow will set up a simple enclosure and mesh it at a resolution to resolve the slits.
Then, it sets up a Gaussian EM wave propagating towards the enclosure, along with a E-Field probe inside the enclosure.
It meshs and runs the simulation, then automatically computes the Shielding Effectiveness and sends it back to STK.

## Slide 11: Setting up Shielding Effectiveness options

## Slide 12
Analyzing Results

## Slide 13: Analyzing Results
Once the simulation has completed, the user can right click the Shielding Effectiveness plot in the tree on the left in Discovery.
Results will also be propagated back to STK (note results in STK are shown in linear scale on the x-axis).

## Slide 14: Analyzing Results