## Slide 1
STK Shield Plus – Surface Charging
Prepared by:
Jason DiMartino – Scientist II
Zach Stevens – Scientist II
Kevin-Druis Merenda – Principal Scientist I and Lead Product Manager

## Slide 2
Demo Background

## Slide 3: Demo Background
Demo Outline
Define a satellite object in STK on which to analyze surface charging effects.
Import satellite CAD into the workflow and define an environment in which to analyze it.
View results of surface charging effects and steady state potential reached.

## Slide 4: Demo Background
Background
EMA’s surface charging workflow in STK Shield Plus is designed to provide fast, convenient access to the power of the BEM plasma surface charging features of Ansys Charge Plus.
Surface charging occurs when spacecraft are exposed to the high energy particle environments around Earth. These particles interact with the surface of the spacecraft and cause charge imbalance, leading to current flows across the surface of the craft, whose effects depend on material properties and the environment to which they are exposed.
These currents eventually level out and reach a steady-state potential, but significant differential potential between materials can cause concern due to possible ESD events.
Such analysis can provide rapid preliminary evaluation of ESD risk for a given spacecraft between easily exchangeable orbits and environments.
This model uses analytical definitions of the plasma environment options, as surface charging problems deal primarily with lower energy plasma components for which databases are not currently available.

## Slide 5
Setting up the STK Scenario

## Slide 6: Setting up the STK Scenario
Open the provided STK Scenario within the folder to retrieve a preset Scenario with the GEO_Sat

## Slide 7: Opening STK Scenario

## Slide 8
Setting up Surface Charging Options

## Slide 9: Setting up Surface Charging options
Click the Surface Charging Options item in the EMA toolbar on the right.
Graph Object: GEO_Sat
Geometry – .dsco file containing satellite geometry from the demo folder (surface_charging_blank.dsco)
Environment: GEO
Auto-Assign Materials: Check this box for now – if you have a model that you have added other material assignments to that you want preserved, un-check this box.
Headless: False – if headless, will run without opening the Shield Plus GUI, reducing some computational overhead
Click Run Workflow to open the Discovery UI and run the solver.

## Slide 10: Surface Charging Options

## Slide 11
Analyzing Results

## Slide 12: Analyzing Results
Once the simulation has completed, the surface potential relative to the plasma can be plotted from the results in the Discovery tree, and will also appear in STK.
In this demo, all materials are defined as aluminum by default and will converge to the same potential. In a practical study, different surface materials would converge to different potentials, which could then be analyzed for ESD risk.

## Slide 13: Analyzing Results
Please caution the slight discrepancy of results piped back to STK – this will be updated soon.

## Slide 14: Analyzing 3D Results
Note that the whole surface of the capsule is at the same potential. This is because it is made of one material – all bodies of the same material will charge to the same potential. If we had different materials on the spacecraft, we would see regions charging differently. An example is shown in the next slide.

## Slide 15: 3D Results with Different Materials – Capsule in LEO